## Slide 1: TREATING MALFUNCTIONS OF HANDGUNS
By: Velarde, Peter D.

## Slide 2: TREATING MALFUNCTIONS OF HANDGUNS

## Slide 3: TREATING MALFUNCTIONS OF HANDGUNS
The Type 1 malfunction is commonly referred to as a failure to feed or a failure to fire. A key symptom is the dreaded click you hear after pressing the trigger. On the range, your immediate response would probably be to stop and wonder what went wrong.

## Slide 4: TREATING MALFUNCTIONS OF HANDGUNS
Common causes for a Type 1 malfunction are a failure to fully seat a magazine, which prevents a round from being stripped into the chamber; a bad round; or the operator’s failure to load the chamber. There are numerous other reasons why you would get a Type 1 malfunction, but these are by far the most common for a properly operating handgun.

## Slide 5: TREATING MALFUNCTIONS OF HANDGUNS
To correct the Type 1, do the following drill: (1) Bring your shooting arm’s elbow back to your ribcage; (2) while keeping the muzzle target-oriented, rotate the ejection port clockwise toward the ground; (3) using the palm of your off-hand, with your fingers pointing up, sharply smack the base of the magazine to ensure it is fully seated; (4) using an overhand grip, rip-rack the slide like you are trying to rip it off of the frame; and (5) reestablish your grip and drive your sights back on target. This drill is often simply referred to as a tap-rack.

## Slide 6: TREATING MALFUNCTIONS OF HANDGUNS

## Slide 7: TREATING MALFUNCTIONS OF HANDGUNS
The Type 2 malfunction is often referred to as a stovepipe or a failure to eject. The key symptom of this malfunction is a dead trigger, meaning when you press the trigger, nothing happens. No click. No bang. Just mush. This malfunction gained the nickname “stovepipe” because, when a fired case fails to properly eject and becomes trapped in the pistol’s ejection port, it looks like a stove’s exhaust pipe.

## Slide 8: TREATING MALFUNCTIONS OF HANDGUNS

## Slide 9: TREATING MALFUNCTIONS OF HANDGUNS
Common causes for a Type 2 malfunction are limp-wristing, or not providing solid enough resistance for the handgun during recoil; impeding the slide during recoil; underpowered ammunition; a broken or malfunctioning extractor or ejector; a malfunctioning magazine; or an overpowered recoil spring. By far the first two examples are the most common causes for a Type 2 malfunction, and they are basically due to operator error. This is a good thing because operator errors are easier to prevent and fix than mechanical failures.

## Slide 10: TREATING MALFUNCTIONS OF HANDGUNS
The response to a Type 2 is identical to that of a Type 1: an aggressive tap-rack. The reason this works is that the next round to feed from the magazine helps push the stovepiped empty case out of the feed port. And with the feed/ejection port rotated toward the ground, gravity helps the case on its way.

## Slide 11: TREATING MALFUNCTIONS OF HANDGUNS
The Type 3 malfunction (commonly called a double feed) is the mother of all malfunctions, short of a stuck case or a catastrophic part failure that renders the handgun inoperable. In the latter two malfunctions, you need to start thinking Plan B. There is no drill to fix them without tools.

## Slide 12: TREATING MALFUNCTIONS OF HANDGUNS
The key symptom of a Type 3 malfunction is identical to that of a Type 2: a dead trigger. In a handgun, a Type 3 is the result of a live round heading into the chamber when another live round is already there.
Common causes of this malfunction essentially involve either an extractor failure, a magazine failure or a stuck case.

## Slide 13: TREATING MALFUNCTIONS OF HANDGUNS
The drill for correcting a Type 3 malfunction is as follows: Without stopping to think or assess, (1) bring your shooting arm’s elbow back to your ribcage; (2) engage the slide stop with your shooting hand’s thumb and, using an overhand grip with your off-hand, rip-rack the slide like you are trying to rip it off of the frame; (3) using your off-hand, rip the magazine from the mag well and throw it to the ground; (4) while keeping the muzzle target-oriented, rotate the ejection port clockwise toward the ground; (5) using an overhand grip, rip-rack the slide three times like you are trying to rip it off of the frame; (6) perform an emergency reload; and (7) reestablish your grip and drive your sights back on target. Rip. Roll. Rack. Reload.